Requirement: The base URL must be configurable at run-time. It is not hard coded. Users should be free to change the base URL as they see fit. If one base URL becomes unavailable then another can be selected. This helps to increase user choice and reduce electronic waste.

Requirement: URL length is configurable. It must not exceed a given limit.

The URL length is constrained by the size of the NFC EEPROM. It cannot exceed this and should not be significantly shorter. URL length depends both on the length of the preamble and the length of the circular buffer.

Feature: Circular buffer length is configurable at compile time. The latter may be limited by RAM on the microcontroller.

Implementation: BUFLEN_BLKS.

Feature: URL length is checked against a limit on startup. If the limit is exceeded an error is raised. This prevents overflow of the NFC EEPROM.

Feature: Preamble length is calculated. It will vary based on the length of the base URL.

Requirement: The encoder must be as simple and lightweight as possible. It is will run on an MSP430 microcontroller and without an RTOS.

Feature: Only static memory allocation is used. The size of the circular buffer is fixed at compile time.

Feature: The encoder is written in C.

Feature: The preamble always occupies an integer number of blocks and is zero-padded where necessary.

Requirement: The decoder must perform the reverse operation of the encoder.

Feature: Each encoder format has a Python wrapper so that it can be tested alongside the decoder.

Implementation: HTEncoder.

Implementation: TEncoder.

Requirement: The codec must support either one or two sensor readings per sample.

Feature: The number of readings per sample is specified by the format parameter.

Requirement: The codec must support sensor readings from more than one sensor type.

Feature: The sensor type, model and manufacturer is specified by the format parameter.

Feature: The URL has a format parameter. It specifies how the circular buffer is decoded.

Requirement: Flash wear should be minimised.

Specification: Frequently changing data are stored in a circular buffer.

Feature: Sensor samples are stored in a circular buffer.

Requirement: The URL must contain only URL-safe characters.

Requirement: The URL decodes to a timestamped series of samples, but it cannot contain an absolute timestamp.

Feature: Timestamps are calculated based on now, timeinterval and elapsed.

Implementation: applytimestamp()

Requirement: Sample timestamps must be precise to 1 minute.

Requirement: Decoder can check if the URL has originated from an authenticated user.

Feature: Integrity and authenticity of the status and circular buffer parameters is enforced with a Hash based Message Authentication Code.

Non-requirement: All parts of the URL protected from tampering by the HMAC.

Feature: The optional HMAC prevents a 3rd party from storing any circular buffer data in a 1st party database without permission. It stops CUPL-sensor manufacturer B from producing hardware that uses the web services of manufacturer A. An encrypted HTTPS connection prevent a 3rd party from intercepting and modifying URL parameters (e.g. time interval) in transit.